## Slide 1: Back to Basics
Principles of Sound

## Slide 2: Overview
A brief history of the Universe of acoustics (Ruth)
Acoustics Intro (Kait)
  Math refresher
Break!
Measurements (Kait)
  Continuous/Impulsive
Python Bootcamp
Reading List, sound measurements and JASCO Pocket guide (reference)
  https://tethys.pnnl.gov/sites/default/files/publications/jmse-09-00173.pdf
  https://www.oceansinitiative.org/wp-content/uploads/2012/07/PocketBook-3rd-ed.pdf

## Slide 3: What is sound
Changes in density (compression and expansion)
Air, water, sound, electromagnetic, gravity

## Slide 4: Critical measures:
Amplitude (A, unitless),
Wavelength (λ, m)
Period (τ,s)
Phase (ϕ, radians)
k - the wave number (1/λ),
ω - angular frequency (π/τ)

## Slide 5: Important Relationships:
c =λf
k=ωc
k=2π/ λ
+
Wave moving +x
Wave moving -x
Some fun. f1
Some fun. f2
Real part (amplitude)
Imaginary/complex part (phase)
f

## Slide 6
MATH BREAKOUT!

## Slide 7
how pressure (previously displacement) varies spatially in all directions.
how pressure changes over time (its second derivative with respect to time)
change in particle velocity leads to a change in pressure. The pressure drives the particle motion, which feeds back into pressure changes, completing the cycle of wave propagation.
if pressure varies spatially, it drives temporal acceleration

## Slide 8: Boundary Conditions
Rigid, fixed; Displacement & velocity=0
Free, pressure release; pressure =0

## Slide 9: Interactions
Most sound combination of different harmonic waves at different amplitudes and frequencies
Results in constructive and destructive interference
Can sum multiple harmonic waves to make any shape

## Slide 10: Measurements
0-to peak
RMS
Peak-to-peak

## Slide 11: Measurements
Intensity- amount of energy transmitted per unit time through a unit area
= specific acoustic impedance, characteristic impedance:
opposition of a medium to wave propagation
𝜌 = (kg/m3)
c = speed of sound in the medium

## Slide 12: Impulsive Signals
Duration over which signal is averaged | rms pressure
0.5 sec | 1.4 µPa
1 sec | 1.0 µPa
2 sec | 0.8 µPa
www.dosits.org

## Slide 13
Metric and Notation | Equation | Usage
Peak sound pressure level (Lpk, L0-pk, or SPLpk) |  | Max instantaneous sound pressure, which is used to assess (PTS) and (TTS) in the hearing of marine mammals, gastrointestinal tract injury in marine mammals, and mortality and injury in fish and sea turtles.
RMS sound pressure SPL(Lp,rms SPLrms) |  | The square root of the average of the sound pressure squared over a given duration to assess potential behavioral disturbance in marine mammals from impulsive and non-impulsive sound
Sound Exposure Level LE or SEL |  | 1-s normalized LE is used to characterize the source level for non-impulsive sound [56]
Single-strike, sound exposure level (LE,ss, or SELss |  | For impulsive or non-impulsive intermittent sounds, this is the LE for a single hammer strike for pile driving [ 56, 57], a single air gun shot for a seismic survey, or a single ping for sonar.
Cumulative sound exposure level (LE, cum or SELcum) |  | LE for the entire duration of sound Exposure. Assess PTS and TTS in marine mammals and the mortality or injury of fish and sea turtles exposed to impulsive sound .
Metric and Notation | Equation | Usage
Peak sound pressure level (Lpk, L0-pk, or SPLpk) |  | Max instantaneous sound pressure, which is used to assess (PTS) and (TTS) in the hearing of marine mammals, gastrointestinal tract injury in marine mammals, and mortality and injury in fish and sea turtles.
RMS sound pressure SPL(Lp,rms SPLrms) |  | The square root of the average of the sound pressure squared over a given duration to assess potential behavioral disturbance in marine mammals from impulsive and non-impulsive sound
Sound Exposure Level LE or SEL |  | 1-s normalized LE is used to characterize the source level for non-impulsive sound [56]
Single-strike, sound exposure level (LE,ss, or SELss |  | For impulsive or non-impulsive intermittent sounds, this is the LE for a single hammer strike for pile driving [ 56, 57], a single air gun shot for a seismic survey, or a single ping for sonar.
Cumulative sound exposure level (LE, cum or SELcum) |  | LE for the entire duration of sound Exposure. Assess PTS and TTS in marine mammals and the mortality or injury of fish and sea turtles exposed to impulsive sound .
https://tethys.pnnl.gov/sites/default/files/publications/jmse-09-00173.pdf